## Slide 1: Emergency Response Solutions

## Slide 2: FFD Initial SCBA Training - Objectives
The objective of this training is to prepare for the safe use of the MSA G1 SCBA in a dynamic, stressful, and constantly changing environment.
Only constant training and practice with the MSA SCBA will “YOU” develop the proficiency needed to operate safely and effectively in a real life situation.

## Slide 3: FFD Initial SCBA Training
Components & Assembly
Donning / Doffing
Cleaning
Maintenance
Daily SCBA Check

## Slide 4: Components
Cylinder
Harness
Regulators
Integrated Pass
Face Piece
HUD (Heads Up Display)

## Slide 5: Pneumatics – Cylinders
MSA SuperLite Cylinders
More than a pound lighter than standard carbon wrapped cylinders
30 minute duration at 4500 psi
Large luminescent band and gauge face improves firefighter visibility
Gauge is calibrated in 100 psi. increments, (i.e. a gauge reading of 20 is read as 20 x 100 or 2000 psi.)

## Slide 6: Carrier & Harness
Cylinder is retained at top and bottom of the carrier.
Cylinder dovetail connection ensures cylinder
is secure at the bottom of carrier
Dovetail also properly positions the cylinder
for simple and easy connection
New stainless steel cylinder band retains
the cylinder at the top of backframe
Cylinder band is fully adjustable for
different size cylinders

## Slide 7: Central Power Supply
Powers all lights, communications and controls from one source
Battery type – lithium ion rechargeable
Battery location places weight low and close to the back for optimum balance and reduced fatigue

## Slide 8: Central Power Supply
Battery status can be checked without powering-on SCBA
Battery can be changed while SCBA is fastened in jump seat
Convenient tool releases battery when inserted into slot
  Need pictures from iPad app & brochure

## Slide 9: Pneumatics – Cylinder Connection
  Cylinder Connection:
  Remote Quick Connection

## Slide 10: Carrier & Harness
Handle at top of back frame Static load rated to 1000lbs
Drag Rescue / carry handles on either side are static load
rated to 500lbs each

## Slide 11: RIT, Rescue, Firefighter Survival
  Buddy lights – six in total – are viewable 360 degrees and help in locating Firefighter
  Color-coding of buddy lights show both air and alarm status
  Reflective shoulder straps and luminescent cylinder band improve visibility

## Slide 12: Carrier & Harness
Form-fit Shoulder Pads are wider, more flexible; Friction Pads prevent slippage
More reflective material improves visibility

## Slide 13: Voice Amp
G1 Speaker Module
Speaker is small, light weight and durable
Automatic On/Off with integrated PASS device
Capable of passing the NFPA Heat and Emersion leakage test
Bluetooth ready

## Slide 14: Carrier & Harness
Adjustable height lumbar pad can be user positioned to fit different body types and forms
Swiveling lumbar pad adjusts to body movements for better weight distribution, balance and comfort

## Slide 15: Pneumatics – 1st Stage Reducer
  Integration of 1st stage reducer, Bell Low Air Warning and URC fitting into one modular assembly
  Mounted low and close to the back for optimum balance and weight distribution

## Slide 16: RIT, Rescue, Firefighter Survival
  MSA URC fitting can be used to transfill between SCBAs
  Waist-mounted ExtendAir 2 EBS “buddy breather” system

## Slide 17: RIT, Rescue, Firefighter Survival
  Rescue light automatically illuminates Universal Rescue Connection in low air situation

## Slide 18: Service Tracking Software
The G1 is equipped with RFID tracking tags attached to all major components including: cylinder, facepiece, regulator, back frame, power module and control module
MSA asset tracking and service tracking software.

## Slide 19: G1 Regulator
  Large dual action buttons remove the regulator and automatically shut off the flow of air

## Slide 20: G1 Regulator
Electronics and Microphones are contained in a sealed module integrated into the regulator while maintaining a small, ergonomic form
  HUD LEDs in the regulator use light pipes to carry light to the facepiece mounted icons
Smart Microphones shut off automatically when no voice signal is detected to conserve battery

## Slide 21: G1 Regulator
  Dual microphones reduce background noise and feedback
  Microphones are protected inside regulator to reduce cost of ownership
  Communications electronics use proprietary algorithms to eliminate amplification of inhalation noise… No Darth Vader effect
Speaker module can be mounted on left or right shoulder

## Slide 22: G1 Integrated PASS

## Slide 23: G1 Integrated PASS
Control Module
Power Module

## Slide 24: G1 Control Module
Opening Screen

## Slide 25: G1 Control Module
Auto-Activation turns on display when control module is lifted
Bright full color display with large numbers provides easy viewing
Built-in Bluetooth allows for integration with future technologies

## Slide 26: G1 Integrated PASS
Control Module
Auto Activation turns on display when control module is lifted
Bright full color display with large numbers allows easy viewing
Built in Bluetooth allows for integration with future technologies
Display settings are customizable

## Slide 27: G1 Control Module
Configurable display to match FFD SOPs
Secondary Thermal Alarm
Time Remaining Alarm
Pressure Drop Alarm
Evacuation Alarm
Low-Battery Alarm

## Slide 28: G1 Control Module
Configurable display to match FFD SOPs
Pressure Change
Primary Thermal Alarm
Motion or Manual Alarm
Pre-Alarm

## Slide 29: G1 Facepiece

## Slide 30: Facepiece Construction
Anti-Fog Lens
Heat Resistance Lens
Hycar Rubber Sealing Surface

## Slide 31: G1 Facepiece
No Electronics In or On the Facepiece
No batteries
Simplifies cleaning
Reduces weight and cost

## Slide 32: G1 Facepiece
Inhalation Check Valve
  Cross contamination protection
  No need to decontaminate the regulator after use
Exhalation Valve in Facepiece
  Opens to allow for release of exhaled breath
  Also ejects moisture build-up
Exhalation Valve

## Slide 33: G1 Facepiece
Inhalation Check Valve
Blocks exhaled air from entering regulator
Open Port
Reduces breathing resistance for standby breathing (off air)

## Slide 34: G1 Facepiece
Head Harness:
Mesh head harness
With neck strap or without
Facepiece & Nose Cups:
Small
Medium
Large

## Slide 35: G1 Facepiece
Speech Diaphragm allows for clean transfer of voice through component housing
Vented Component Housing

## Slide 36: G1 Facepiece
Heads Up Display (HUD)
Uses light pipes to illuminate icon indicators
Colour coded icons show battery, evacuation and alert status
Speech Diaphragm
Aligns with wearer’s mouth
to provide clear, intelligible
speech either on or off air

## Slide 37: G1 Facepiece
Heads-Up Display
  Light pipes transfer light into HUD windows
  Right side provides air management information
  Left side provides icons as system status indicators
    (Includes Battery Icon, Evacuation Icon and PASS Pre-Alarm Icon)

## Slide 38: HUD
• 4 green LED — Start-up or 100% displayed for 20 seconds before going out.
• 3 green LED — 75% displayed for 20 seconds before going out.
• 2 yellow LED — 50% begins flashing continuously with audio beep.
• 1 red LED — 0 to 35% activate and stay flashing accompanied by low pressure alarm until unit is shut down.
HUD activated anytime green button pushed

## Slide 39: Accessory Equipment
Transfill Hose & Pouch
Spectacle Kit
APR Adapter

## Slide 40: Cleaning & Disinfecting Face Piece
Wash Face Piece and nose cup in “Confidence Plus” cleaning solution or mild dish soap
Rinse thoroughly with clean water
  Water temp. should not exceed 100 deg.
Towel dry bulk water
Purge exhalation valve
Replace nose cup and hang to dry

## Slide 41: Cleaning & Disinfecting Pack
Rinse pack (battery needs to remain in Pack)
Brush with soapy water
Rinse thoroughly with clean water
Purge regulator
Towel dry bulk water (Inspect)
Air dry on apparatus

## Slide 42: Daily SCBA Mask Check
1 Check the amount of air in cylinder and
replace if pressure indicator is below 4000
psi.

## Slide 43: Daily SCBA Mask Check
2 Adjust shoulder & waist straps to fully open.
Set lumbar pad height to high, medium, or
low for personal fit.

## Slide 44: Daily SCBA Mask Check
Confirm BUDDY-BREATHING HOSE is properly stowed.

## Slide 45: Daily SCBA Mask Check
Confirm BYPASS KNOB is in the closed position.
  Rotated clockwise against housing

## Slide 46
Daily SCBA Mask Check
5 Press DONNING SWITCH.

## Slide 47
Daily SCBA Mask Check
6 Open cylinder valve all the way and listen
for low air-warning signals.
✔Check Battery Level
✔Primary low air warning will ring
✔Pass device will chirp and light to confirm
operation
✔Verify HUD device will light up and show bar
indicators
✔Check Lights on backframe

## Slide 48: Daily SCBA Mask Check
7 Pause approximately 18-20 seconds and
confirm pass device motion alarm
activates.

## Slide 49: Daily SCBA Mask Check
8 Hold face piece to face establishing a good
seal, inhale to start. Take a couple breaths
to confirm proper operation.

## Slide 50: Daily SCBA Mask Check
9 Press donning switch before removing face
piece from face.

## Slide 51: Daily SCBA Mask Check
10 Close air cylinder all the way and listen for
any air leaks. (1 minute)

## Slide 52: Daily SCBA Mask Check
11 Open bypass knob slowly and listen for
low air warning signals to sound at 33% of
remaining cylinder pressure on pressure
gauge. Indicated by red zone on pressure
gauge

## Slide 53: Daily SCBA Mask Check
12 Return SCBA to ready to use position.

## Slide 54: Daily SCBA Mask Check
13 Record check in station journal and initial.

## Slide 55: Daily SCBA Mask Check
14 Report any irregularities or discrepancies
to your supervisor

## Slide 56: Daily SCBA Mask Check
CAUTION: SCBA tank can bleed down if cylinder valve is not completely closed when stowed.

## Slide 57
Questions?

## Slide 58
THANK YOU!